## Slide 1
Validation of S5P tropospheric ozone OFFL v01.01.05 using ozonesonde data
Daan Hubert1, Tijl Verhoelst1, Arno Keppens1 and Jean-Christopher Lambert1
Acknowledgements to A. M. Thompson2, J. C. Witte2,3 , B. J. Johnson4 and all SHADOZ contributing stations and instrument PI’s
Thanks to K.-P. Heue5, D. Loyola5 and K.-U. Eichmann6 for useful discussions
(1) Royal Belgian Institute for Space Aeronomy (BIRA-IASB), BE (2) NASA GSFC, USA (3) SSAI, USA (4) NOAA, USA (5) DLR, DE (6) IUP Bremen, DE
Co-funded by ESA S5P MPC and BELSPO/BIRA-IASB

## Slide 2: S5p CCD data record
L2_O3_TCL CCD OFFL v01.01.05 from ESA HUB
  444 products available : 9 Nov 2017 – 7 Feb 2019
Product details
  Partial O3 column surface – 270 hPa
  20°S-20°N
  0.5° lat x 1° lon x 3 days
Screening
  Remove products that [do not span 6±0.5 days] (v01.01.02: 5±0.5) OR [have double start and/or end date]  removes 69 products (=15.5%)
  Remove grid cells with qa_value≤0.7 (v01.01.02: <0.5)  removes 15.9% cells, mostly poleward of 15°

## Slide 3: One year of S5p tropospheric ozone data

## Slide 4: Biases between neighbouring lat bands
Often, ΔSOC between neighbouring bands is 1-2 DU.
Leaves clear imprints on TTOC fields.

## Slide 5: CCD fields follow progression S5p orbit

## Slide 6: FRM data records : ozonesonde
In-situ reference data from SHADOZ & NOAA ozonesonde archives
Vertically resolved O3 profiles from surface to ~30km
9 sites with ~(bi)weekly sounding during S5p period, 364 profiles.
Data are very well characterized (Witte et al., 2017, 2018; Thompson et al., 2018; …)
Screening as in Hubert et al. (2016).
Convert each sonde profile to S5p CCD like information: partial column between surface and 270 hPa
Produced by Multi-TASTE (BIRA-IASB)

## Slide 7
biomass
convection
Time series of tropospheric ozone columns for S5P OFFL v01.01.05 (3 day cell) and ozonesonde (single flight trajectory).
All data are shown.
Zonal wave-one & annual patterns are present.
S5P OFFL O3_TCL CCD v01.01.05 versus ozonesonde
Produced by Multi-TASTE (BIRA-IASB)

## Slide 8
Restrict to ozonesonde data averaged over associated S5P time window(s).
Most direct comparison.
Correlations are reasonable, not great.
Caveat : time & horizontal sampling of sonde is poorer.
S5P OFFL O3_TCL CCD v01.01.05 versus ozonesonde
Produced by Multi-TASTE (BIRA-IASB)

## Slide 9
Time series of absolute difference S5P – ozonesonde.
Median & mean statistics generally similar.
S5p overestimates wrt sonde, range: -0.8…+6.3 DU.
Spread in comparisons ranges between 2.3…7.1 DU.
S5P OFFL O3_TCL CCD v01.01.05 versus ozonesonde
Produced by Multi-TASTE (BIRA-IASB)

## Slide 10
Time series of relative difference (S5P/ozonesonde)–1.
Median & mean statistics generally similar.
S5p overestimates wrt sonde at all but one site, range -3...+34%.
Spread in comparisons ranges between 10…38%.
S5P OFFL O3_TCL CCD v01.01.05 versus ozonesonde
Produced by Multi-TASTE (BIRA-IASB)

## Slide 11
Summary statistics : S5P OFFL O3_TCL CCD v01.01.05 versus ozonesonde
Produced by Multi-TASTE (BIRA-IASB)
mission requirement bias

## Slide 12: First exploration of random uncertainty
Observed spread = 5.4 DU
Reported stddev SOC = 3.2 DU
Stddev over 3-day window = 1-2 DU
Reported stddev of stratospheric ozone column is 3 DU = ~10-15%.
Is mission requirement of 10% (~2 DU) too ambitious?

## Slide 13: Conclusions CCD : OFFL v01.01.05
Almost each product contains artificial (lat x lon) structures related to sampling
  Bias between neighbouring latitude bands (<1-2 DU).
  Bias follows progression of S5p orbit.
Comparison of 364 S5p products to 359 ozonesonde profiles shows
  Moderate-strong correlation of 63%.
  Positive bias for S5p at all (but one) SHADOZ sites: mean value is 16±4% or 3.1±0.8 DU.
  Comparison spread ranges from 10-38% or 2.3-7.1 DU.
  Caveat: keep in mind that sampling differs substantially for S5p and sonde

## Slide 14: Conclusions CCD : OFFL v01.01.05
Assessment wrt product requirements
Bias : network mean value of +16% is within required 25%, requirement is not met at 2/9 sites.
Random : required 10% smaller than observed spread, but the impact of sampling needs more analysis.
Recommendation : release!
But with clear disclaimer (sampling artefacts, bias, spread) in PRF.